## Slide 1
SeaNergy
Adaptive sonar transmission for changing water
SIH 2026 | PS 26058 | TEAM HYPER GREY
PROPOSED SOLUTION
SeaNergy is a sensor-informed, software-defined sonar transmitter payload for AUVs, designed to turn changing water conditions into a tailored acoustic ping. It models the channel, selects frequency, bandwidth, duration and power, then synthesizes the waveform for an efficient transmit chain while recording why that pulse was chosen.
FROM WATER TO PING
01
Read the water
Temperature, TDS and turbidity readings, plus a depth input, describe the conditions for each ping.
02
Choose the pulse
The physics model estimates speed and loss, then scores frequency, bandwidth, duration, level and window.
03
Build the waveform
CW, LFM, geometric sweep and Barker-13 signals are generated and inspected in software.
04
Deliver and verify
The timer/DMA-to-DAC output path is designed for stable ultrasonic transmission. Scope and tank tests are next.
WHY THE NEED?
An AUV crosses water whose temperature, salinity, depth and turbidity vary. Those changes alter sound speed and acoustic loss, so one preset ping cannot always balance useful range, target detail and energy. The challenge is to retune each pulse in real time without tying up the vehicle’s processor.
PS 26058: CURRENT PROOF AND NEXT TEST
PS REQUIREMENT | CURRENT EVIDENCE | NEXT VALIDATION
Water inputs | T, TDS, turbidity and controls | Calibrated marine channels
Dynamic waveforms | Four families generated in software | Mode switching on a scope
Low-power output | DMA design and power model | Current and tank measurements
Prototype status: sensing and waveform software operate today; adaptive ultrasonic output awaits bench validation.
Notes: Sources: SeaNergy executive-summary.pdf and PS 26058 compliance-matrix.pdf in this repository. The AUV hero image is a generated concept illustration, not a photograph of the prototype. The four waveform families and bench sensor inputs are current software/bench evidence. DMA-driven ultrasonic output, scope tests, and tank measurements remain planned.