## Slide 1
SeaNergy
Adaptive sonar transmission for changing water
SIH 2026 | PS 26058 | TEAM HYPER GREY
PROPOSED SOLUTION
SeaNergy is a sensor-informed, software-defined sonar transmitter payload for AUVs, designed to turn changing water conditions into a tailored acoustic ping. It models the channel, selects frequency, bandwidth, duration and power, then synthesizes the waveform for an efficient transmit chain while recording why that pulse was chosen.
FROM WATER TO PING
01
Read the water
Temperature, TDS and turbidity readings, plus a depth input, describe the conditions for each ping.
02
Choose the pulse
The physics model estimates speed and loss, then scores frequency, bandwidth, duration, level and window.
03
Build the waveform
CW, LFM, geometric sweep and Barker-13 signals are generated and inspected in software.
04
Deliver and verify
The timer/DMA-to-DAC output path is designed for stable ultrasonic transmission. Scope and tank tests are next.
WHY THE NEED?
An AUV crosses water whose temperature, salinity, depth and turbidity vary. Those changes alter sound speed and acoustic loss, so one preset ping cannot always balance useful range, target detail and energy. The challenge is to retune each pulse in real time without tying up the vehicle’s processor.
MODELLED RESPONSE: 5 TO 1,000 NTU
PARAMETER | 5 NTU | 1,000 NTU
Centre frequency (kHz) | 351 | 148
Bandwidth (kHz) | 299 | 96
Range resolution (mm) | 2.6 | 8.0
Modelled sweep, not tank measurements. Sensing and waveform software operate; adaptive ultrasonic output awaits bench validation.
Notes: Sources: SeaNergy executive-summary.pdf and PS 26058 compliance-matrix.pdf in this repository. Numeric table: compliance matrix C-05 modelled water sweep from 5 to 1,000 NTU. Values are not tank measurements. The AUV hero image is a generated concept illustration, not a photograph of the prototype. Four waveform families and bench sensor inputs are current software/bench evidence. DMA-driven ultrasonic output, scope tests, and tank measurements remain planned.