## Slide 1
SeaNergy
Adaptive sonar TX and RX for changing water
SIH 2026 | PS 26058 | TEAM HYPER GREY
PROPOSED SOLUTION
SeaNergy is a sensor-informed TX/RX sonar system for AUVs. Five water inputs guide software selection of frequency, bandwidth, duration and waveform. The transmitter drives an acoustic element, while a separate receiver captures ADC samples for waveform and FFT analysis. Both sides are visible, from the chosen pulse to the received signal.
FROM WATER TO PING
01
Sense five conditions
Temperature, TDS/salinity, turbidity, pH and depth feed the water model.
02
Adapt the TX pulse
The solver scores frequency, bandwidth, duration and level; four waveform modes run in software.
03
Transmit the signal
The TX bench path drives an acoustic element. Adaptive DDS/DMA output remains a scope target.
04
Capture and analyse RX
The receiver records 4,096 ADC samples per frame, then displays the waveform and FFT.
WHY THE NEED?
An AUV crosses water whose temperature, salinity, turbidity, pH and depth vary. These affect sound speed, absorption and scattering, so one preset ping cannot always balance range, detail and energy. Receiving the echo lets us inspect how the chosen pulse behaved.
MODELLED RESPONSE: 5 TO 1,000 NTU
PARAMETER | 5 NTU | 1,000 NTU
Centre frequency (kHz) | 351 | 148
Bandwidth (kHz) | 299 | 96
Range resolution (mm) | 2.6 | 8.0
Modelled sweep, not tank measurements. TX and RX paths exist; adaptive end-to-end underwater performance awaits validation.
Notes: Sources: SeaNergy mobile app 2.2.0 README and adaptation code for pH/depth; TX bench firmware and RX capture firmware/Python viewer; compliance matrix C-05 for modelled 5-to-1,000 NTU sweep. The five water inputs include temperature, TDS/salinity, turbidity, pH and depth. Current repository TX and RX benches are separate; adaptive end-to-end underwater operation has not been validated. Numeric table values are modelled, not tank measurements. The AUV hero image is a generated concept illustration, not a photograph of the prototype.