## Slide 1
SeaNergy
Adaptive sonar TX and RX for changing water
SIH 2026 | PS 26058 | TEAM HYPER GREY
PROPOSED SOLUTION
SeaNergy lets an AUV design its next sonar ping for the water it is actually in. Temperature, salinity, turbidity, pH and depth feed a model that chooses frequency, bandwidth, duration and waveform to balance reach, detail and energy. A TX bench demonstrates acoustic output, while a separate RX chain records samples and shows the waveform and spectrum. Together, they provide a testable path toward real-time adaptive sonar on compact AUV hardware.
WHAT SEANERGY BRINGS
Water-aware pulse design
Five water inputs inform the acoustic model, so pulse settings reflect current conditions instead of a fixed preset.
Four waveform choices
CW, LFM chirps, geometric sweeps and Barker-13 coding offer different ways to balance range, detail and signal quality.
Compact transmitter architecture
The ESP32 TX bench proves the embedded path; timer and DMA streaming define the low-power hardware target.
Visible receiver evidence
A separate RX chain captures ADC samples and displays waveform and FFT views for signal inspection and tuning.
WHY THE NEED?
PS 26058 asks for a low-power AUV transmitter that changes its waveform in real time. A fixed ping must cross water whose temperature, salinity, depth, pH and suspended particles vary. These conditions change travel time and signal loss, while battery and CPU limits constrain every transmission.
WATER CHANGES SOUND SPEED
CHANGE IN WATER | APPROX. SPEED SHIFT
+1 °C temperature | +4.5 m/s
+1 ppt salinity | +1.3 m/s
+100 m depth | +1.7 m/s
NOAA sound-speed sensitivities. TX and RX benches are separate; adaptive underwater performance awaits validation.
Notes: Sources: SIH PS 26058 clauses C-01 to C-05 and C-08 in the project's compliance matrix; SeaNergy mobile app 2.2.0 README, adaptation and DSP code for pH/depth and four software waveform modes; TX bench firmware and RX capture firmware/Python viewer. The table's approximate sound-speed sensitivities are from NOAA, https://repository.library.noaa.gov/view/noaa/44869/noaa_44869_DS1.pdf (temperature +4.5 m/s per +1 C, salinity +1.3 m/s per +1 ppt, pressure/depth +1.7 m/s per +100 m). These are general seawater reference values, not SeaNergy measurements. The TX and RX benches are separate; adaptive end-to-end underwater operation has not been validated. The AUV hero image is a generated concept illustration.